## Slide 1
Product Six View—UF3-S

## Slide 2
Product Packaging and Accessories Description - UF3-S
Packing List:
Reader*1
Power adapter (with tail plug)*1
WIFI, Bluetooth antenna stick *1
Main and auxiliary 4G antenna stick*2
GPS positioning antenna*1
GPIO interface plug-in*1
Wall mounting expansion screw *1 pack

## Slide 3
Product Interface Description—UF3-S
Front: RFID antenna interface *8——(Interface type: SMA female port) Left side:
GPS antenna interface *1——(Interface type: SMA female) 4G antenna interface*2——(main and auxiliary dual antennas, interface type: SMA female port) WIFI/Bluetooth antenna interface*1——(SMA female port) SIM interface*1——(Micro SIM card) Right side:
Micro USB*1——(R&D and debugging, wired flashing) USB*2——(Support OTG, can be connected to an external USB stick, keyboard, mouse) RESET*1——(Pin click the information screen, long press to restart) Back:
GPIO*1——(General Purpose Input/Output) RS232*1——(DB9 female port, serial communication) RJ45*1——(Network Communication) HDMI*1——(Screen output, support 1920x1080P) USB*1——(Support OTG, can be connected to an external USB stick, keyboard, mouse) POWER*1——(DC DC power input)

## Slide 4
How the product works—UF3-S
Android DEMO: Display + HDMI cable + reader (RFID antenna + wired mouse)

## Slide 5
How the product works—UF3-S
Bluetooth DEMO: PDA (Android) + reader (RFID antenna + Bluetooth antenna）

## Slide 6
How the product works—UF3-S
Host computer DEMO (network port, serial port): Host computer (windows platform) + communication line (network cable, serial port line) + reader (RFID antenna)

## Slide 7
How the product works—UF3-S
MDM configuration group issuance: (parameter class, can not perform read and write operations such as inventory)